## Slide 1
CET203A Digital Electronics
and Logic Design
DEPARTMENT OF COMPUTER SCIENCE AND ENGINEERING

## Slide 2: CET203A Digital Electronics and Logic Design
Examination scheme: Total Marks-100
- 50 Marks Continuous Assessment
- 50 Marks End Examination
Course Objectives:
To gain knowledge of characteristics of Logic Families and design Combinational Circuits
To design and implement Sequential Circuits
To realize sequential circuits using concepts of ASM chart.
To design and implement digital circuits using Hardware Description Language.
2

## Slide 3: CET203A Digital Electronics and Logic Design
Course Outcomes:
Design sequential circuits using Flip flops and Registers.
Devise applications using ASM chart and concept of Moore, Mealy machine.
Implement combinational and sequential circuits using Integrated Circuits.
Implement combinational and sequential circuits using VHDL program.

## Slide 4: Syllabus
Combinational Logic Design: Characteristics of Digital ICs: Speed, power dissipation, figure of merit, fan-in, fan-out, Current and voltage parameters, Noise immunity, operating temperature range. Minimization of SOP and POS equations using K-Maps up to 4 variables. Multiplexers, MUX (IC 74153), MUX tree, De-multiplexers, Decoder (IC74138). Implementation of Half- Adder, Full Adder using MUX and Decoder.
Sequential Logic Design: SR, JK, MS JK, D, T Flip Flops. Truth Tables and Excitation tables. Conversion from one type to another type of Flip Flop. Study of IC7476. Counters: 3 bit up, 3bit down Asynchronous and Synchronous counter. Study of Modulus n counter, IC 7490 and its application to implement MOD Counters. Registers: Buffer register, shift register types-SISO, SIPO, PISO, PIPO. Ring counters, Johnson Counter.
Synchronous Sequential Circuit Design: State diagram, State Tables, State assignment. Moore and Mealy Machine representations, sequence detector using Mealy model. Algorithmic State Machines (ASM): Finite State Machines (FSM). ASM charts, notations, construction of ASM chart (e.g. Counters, sequence detector for Moore and Mealy model).
Introduction to Very High Speed Integrated Circuit Hardware Description Language (VHDL): Introduction to VHDL, Library, Packages, Entity, Architecture, Data Objects (Variables, Signals, and Constants), Data Types, Data Operators and VHDL Modeling styles with Programming Examples – Dataflow, Behavioral and Structural. Comparison of modeling styles. Concurrent Statements (When..Else), Sequential statements (If..Else, Loop) Comparison of Concurrent and Sequential statements.

## Slide 5: Syllabus (Contd..)
List of Assignments:
To Realize 3 bit Binary to Gray and 3 bit Gray to Binary code converter using Logic Gates.
Realize following functions using IC 74153
a) Half adder b) 8:1 Mux ( Σ m (0,2,4,7) )
Design and implement 3 bit Synchronous Up Counter using IC7476.
Design and implement MOD 10, MOD 100 and MOD N counter using IC 7490.
Draw ASM chart for real life digital system ( e.g. Washing Machine, Vending Machine, Elevator control, ATM machine).
Design & simulate 4 bit up/down synchronous counter using Behavioral modeling in VHDL.
Design & simulate 4:1 Multiplexer using Dataflow modeling in VHDL.
Design & simulate Full adder using structural modeling in VHDL.

## Slide 6: Syllabus (Contd..)
Text Books:
R.P. Jain, “Modern Digital Electronics”, McGraw Hill Education,2012, ISBN–13: 978-0-07- 066911-6., 4th edition
J. Bhaskar , “A VHDL Primer”,: Pearson Education, 2008, ISBN: 9788177582000, 3rd Edition
Reference Books:
Morris Mano, “Digital Logic & Computer Design”, Pearson Education ( Link: https://viden.io/knowledge/114/attachments/427?name=viden-K105-Digital+Logic+And+Computer+Design+By+M.+Morris+Mano+%282nd+Edition%29.pdf)
D. Leach, Malvino, Saha, “Digital Principles and Applications”, Tata McGraw Hill, 2011, ISBN – 13:978-0-07-014170-4. , 7th edition
Thomas Floyd, “Digital Fundamentals”, Pearson Education, 2003, ISBN 8178088762, 8th Edition

## Slide 7
Assessment Scheme:
Class Continuous Assessment (CCA) (Max marks 50)
Assignments | Mid Term Test | Presentations | PBL Activity/Case study | MCQ | Oral | Attendance
15% | 30% | - | 15% | 20% | - | 20%
10 Marks | 15 Marks | -- | 10 Marks | 10 Marks |  | 5 Marks
Laboratory Continuous Assessment (LCA) (Max marks 50)
Assessment through Rubric (60%) | End term Practical/oral exam (40%)
30 | 20

## Slide 8: Syllabus: Module 1
Combinational Logic Design: Characteristics of Digital ICs: Speed, power dissipation, figure of merit, fan-in, fan-out, Current and voltage parameters, Noise immunity, operating temperature range. Minimization of SOP and POS equations using K-Maps up to 4 variables. Multiplexers, MUX (IC 74153), MUX tree, De-multiplexers, Decoder (IC74138). Implementation of Half- Adder, Full Adder using MUX and Decoder.
Course Objectives:
1) To gain knowledge of characteristics of Logic Families.
2) To design Combinational Circuits.
Course Outcomes:
1) Design combinational circuits using gates and MSI ICs.

## Slide 9
Combinational Logic Design

## Slide 10: Introduction to Digital Electronics & Logic Design
What is Signal ?
Types of Signal
  Analog Signal
  Digital Signal

## Slide 11: Typical Signal Processing System
ADC
Digital System
DAC
Analog In
Analog Out
Computer
Calculator
Watch
Measuring Instrument

## Slide 12: Typical Signal Processing System in Details

## Slide 13: Advantages of Digital Systems Over Analog Systems
Reproducibility of the results.
Accuracy of results.
More reliable than analog systems due to better immunity to noise.
Ease of design: No special math skills needed to visualize the behavior of small digital (logic) circuits.
Flexibility and functionality.
Programmability.
Speed: A digital logic element can produce an output in less than 10 nanoseconds (10-8 seconds).
Economy: Due to the integration of millions of digital logic elements on a single miniature chip forming low cost integrated circuit (ICs).
Uses less Bandwidth.
Efficiency in long distance transmission.

## Slide 14: Inside a Digital System
Digital Systems
Modules
Sub modules
Basic Units(Logic Gates)
Circuits( Transistor, resister, Capacitor etc.)

## Slide 15: Boolean Logic Gates (Building Blocks for Digital Circuits ) (Because Switches are Hard to Work With)
“Logic gates” are better digital circuit building blocks than switches (transistors), Why?...

## Slide 16: Integrated Circuits
The building blocks of computers
Designed for specialized functions
  Examples: the CPU, bus interface, memory management unit
Transistors: primary components of ICs
  Motorola MPC 7400 PowerPC modules: 6.5 million transistors in less than ½ in2

## Slide 17: Integrated Circuits
An IC is nothing but - a number of logic gates fabricated on a single silicon chip.
ICs can be classified according to how many gates they contain
SSI, MSI, LSI, VLSI, ULSI, GSI

## Slide 18
SOP & POS

## Slide 19: Standard Representations for Logic Functions
Logic functions are expressed in terms of logical variables.
Logic function and logic circuit are used synonymously.
A logic circuit is a circuit that executes a processing or controlling function in a computer. This circuit implements logical operations on information to process it.
Logic circuit utilize two values for a given physical quantity (voltage, for example) to denote the Boolean values true and false or 1 and 0 respectively. Logic circuits have inputs, as well as having outputs which can be dependent on the inputs.

## Slide 20
Values of logic variables and logic functions are in binary form( 1 and 0). Any logic function can be expressed in the forms of
1. Sum of Products form (SOP) and
2 Product of Sums form (POS)
E.g. Y= AB + AC’ + BC------------SOP
Y= (A +C)(B + C’)-----------POS

## Slide 21: Standard Representations for Logic Functions
Canonical Normal Form
  Standard form for Boolean expression that provide a unique signature
  If each term in SOP and POS forms contains all the literals then these are known as canonical SOP and POS respectively.
  Each individual term in canonical SOP form is called as minterm and in canonical POS form as maxterm.

## Slide 22: Canonical or Conventional form

## Slide 23: Sum of Product (SOP)
It is a Disjunctive Normal form or Minterm Expansion
E.g.
AB + CD
(A AND B) OR (C AND D)
i.e. OR of AND terms

## Slide 24: Summation Form
  Each individual term in canonical SOP form is called as minterm and in canonical POS form as maxterm.
Summation form is obtained by referring to each minterm in the expression by it’s numerical equivalent in domain, rather than by the list of variables
In this case we substitute a “1” for all positive variables & a “0” for all inverted
All missing variables (i.e. if in AC, B is missing), we have to expand means include all variables, so AC would be ABC + AB’C
Minterms

## Slide 25: Conversion Process
It takes 3 steps:
Each minterm is converted into it’s binary equivalent.
2. Each minterm is converted from binary to decimal.
3. Finally the min terms are placed in ascending order

## Slide 26: Advantages of Summation form
It is useful for implementation in Programmable Logic
One more advantage is that very long & complex expressions can be easily described
Useful for implementation with hardware devices

## Slide 27: Conversion from Conventional to Summation Form

## Slide 28: Conversion from Conventional to Summation Form

## Slide 29: Practice Examples

## Slide 30: Practice Examples

## Slide 32: Practice Examples(Contd..)

## Slide 33: Practice Examples(Contd..)

## Slide 34: Practice Examples(Contd..)

## Slide 35: Practice Examples(Contd..)

## Slide 36: Practice Examples(Contd..)
CSE203 Digital Electronics and Logic Design

## Slide 37: Practice Examples(Contd..)
CSE203 Digital Electronics and Logic Design

## Slide 38: Product of Sum (POS)
It is a Conjunctive Normal form or Maxterm Expansion
E.g.
(A+B) (C+D)
(A OR B) AND (C OR D)
i.e. AND of OR terms

## Slide 39: POS Contd..
A+B+C
A+B+C’
A+B’+C’

## Slide 40: POS (Contd..)

## Slide 41: POS (Contd..)

## Slide 42: Practice Example

## Slide 43: Practice Example

## Slide 44: Practice Example (Contd..)
POS Representation
Y = (M1, M3)
Y= M(1,3)
SOP Representation
Y=∑m(0,2)

## Slide 45: Practice Example (Contd..)
For following truth table find minterm & maxterm i.e. SOP & POS forms
A | B | C | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
m0 0
M1 1
m2 2
m3 3
M4 4
M5 5
m6 6
m7 7
Y (A,B,C) = ∑m(0,2,3,6,7)
Y (A,B,C) = πM(1,4,5)

## Slide 46: Practice Example (Contd..)
For following truth table find summation & product forms i.e. SOP & POS forms
A | B | C | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
m0 0
M1 1
m2 2
m3 3
M4 4
M5 5
m6 6
m7 7
Y (A,B,C) = ∑m(0,2,3,6,7)
Y (A,B,C) = πM(1,4,5)

## Slide 47: Practice Example (Contd..)

## Slide 48: Practice Example (Contd..)

## Slide 49: Practice Example (Contd..)

## Slide 50: Practice Example (Contd..)
Y(A,B,C) = πM(1,4,5)

## Slide 51
K-MAP

## Slide 52: Introduction
Sometimes it is difficult to be sure that a logic expression can be simplified.
Solution is K-Map
A Karnaugh map (K-Map) is a pictorial method used to minimize Boolean expression without having to use Boolean algebra theorems & equation manipulation
It is a special version of truth table
Using K-Map, expressions with 2 to 4 variables are easily minimized

## Slide 53: Introduction (Contd..)
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
00
01
11
10
0
1
A
BC
MSB
LSB
0
1
2
3
4
5
6
7

## Slide 54: 2 – Variables K- Map
0
1
2
3

## Slide 55: 3 – Variables K- Map
0 | 1 | 3 | 2
4 | 5 | 7 | 6
00 01 11 10
BC
A
0
1
A+B+C | A+B+C’ | A+B’+C’ | A+B’+C
A’+B+C | A’+B+C’ | A’+B’+C’ | A’+B’+C
00 01 11 10
BC
A
0
1
A’B’C’ | A’B’C | A’BC | A’BC’
AB’C’ | AB’C | ABC | ABC’
00 01 11 10
BC
A
0
1
SOP Form
POS Form

## Slide 56: 4 – Variables K- Map
0 | 1 | 3 | 2
4 | 5 | 7 | 6
12 | 13 | 15 | 14
8 | 9 | 11 | 10
AB
00 01 11 10
CD
00
01
11
10
AB
00 01 11 10
CD
00
01
11
10
A’B’C’D’ | A’B’C’D | A’B’CD | A’B’CD’
A’BC’D’ | A’BC’D | A’BCD | A’BCD’
ABC’D’ | ABC’D | ABCD | ABCD’
AB’C’D’ | AB’C’D | AB’CD | AB’CD’
A+B+C+D | A+B+C+D’ | A+B+C’+D’ | A+B+C’+D
A+B’+C+D | A+B’+C+D’ | A+B’+C’+D’ | A+B’+C’+D
A’+B’+C+D | A’+B’+C+D’ | A’+B’+C’+D’ | A’+B’+C’+D
A’+B+C+D | A’+B+C+D’ | A’+B+C’+D’ | A’+B+C’+D
SOP Form
POS Form

## Slide 57: Practice Examples
Prepare Truth Table for following K - Map
0 1 | 1 | 3 | 2
4 | 5 1 | 7 1 | 6
12 1 | 13 | 15 1 | 14 1
8 | 9 1 | 11 | 10
00
01
11
10
00
01
11
10
BA
DC

## Slide 58
Row | D | C | B | A | Y
0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
2 | 0 | 0 | 1 | 0 | 0
3 | 0 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 1
6 | 0 | 1 | 1 | 0 | 0
7 | 0 | 1 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 1
10 | 1 | 0 | 1 | 0 | 0
11 | 1 | 0 | 1 | 1 | 0
12 | 1 | 1 | 0 | 0 | 1
13 | 1 | 1 | 0 | 1 | 0
14 | 1 | 1 | 1 | 0 | 1
15 | 1 | 1 | 1 | 1 | 1

## Slide 59: Representation of canonical SOP form on K-Map

## Slide 60: Representation of canonical SOP form on K-Map
Y= A’B’C + A’BC’ + AB’C’ +ABC
0 | 1 | 0 | 1
1 | 0 | 1 | 0
00 01 11 10
BC
A
0
1

## Slide 61: Representation of canonical SOP form on K-Map (Contd..)
AB
00 01 11 10
CD
00
01
11
10
0 1 | 1 | 3 | 2
4 | 5 1 | 7 1 | 6
12 1 | 13 | 15 1 | 14 1
8 | 9 1 | 11 | 10
Y = A’B’C’D’ + A’BC’D + A’BCD + AB’C’D + ABC’D’ + ABCD+ ABCD’

## Slide 62: Representation of canonical POS form on K-Map

## Slide 63: Representation of canonical POS form on K-Map (Contd..)
AB
00 01 11 10
CD
00
01
11
10
0 1 | 0 | 3 0 | 2 0
4 0 | 5 1 | 7 1 | 6 0
12 1 | 13 0 | 15 1 | 14 1
8 0 | 9 1 | 11 0 | 10 0

## Slide 64: Representation of canonical POS form on K-Map (Contd..)
AB
00 01 11 10
CD
00
01
11
10
0 1 | 0 | 3 0 | 2 0
4 0 | 5 1 | 7 1 | 6 0
12 1 | 13 0 | 15 1 | 14 1
8 0 | 9 1 | 11 0 | 10 0
Y= (A + B + C + D’) (A + B + C’+D’) (A + B + C’ +D)
(A + B’ + C + D) (A + B’ + C’ + D) (A’ + B’ + C + D’)
(A’ + B + C + D) (A’ + B + C’ + D’) (A’ + B + C ‘+ D)
Y=πM( 1,2,3,4,6,8,10,11,13 )

## Slide 65: Simplification of Logic function using K-Map

## Slide 66: Example

## Slide 67: Example (Contd..)

## Slide 68: Example (Contd..)
1 |  | 1 | 1
 | 1 | 1 | 1
A
BC
00
01
11
10
0
1
Z = A’C’ + AC + B

## Slide 69: Example (Contd..)

## Slide 70: Example (Contd..)
Y = A’C’ + AC

## Slide 71: Four Adjacent ones
0 1 | 4 | 12 | 8 1
1 1 | 5 | 13 | 9 1
3 1 | 7 1 | 15 1 | 11 1
2 | 6 | 14 | 10
AB
00
01
11
10
00
01
11
10
CD

## Slide 72: Four Adjacent ones (Contd..)
Y = B’C’ + CD
0 1 | 4 | 12 | 8 1
1 1 | 5 | 13 | 9 1
3 1 | 7 1 | 15 1 | 11 1
2 | 6 | 14 | 10
00
01
11
10
00
01
11
10
CD
AB

## Slide 73: Four Adjacent ones (Contd..)

## Slide 74: Four Adjacent ones (Contd..)

## Slide 75: Four Adjacent ones (Contd..)

## Slide 76: Four Adjacent ones (Contd..)
= A’B’CD + A’BCD + ABCD + AB’CD
= CD(A’B’ + A’B + AB + AB’)
= CD [ A’ ( B’ + B) + A (B+B’)]
=CD(A’ + A)---------------------------------(A+A’)=1
=CD

## Slide 77: Prime Implicant
The process of simplification involves grouping of Minterms & identifying Prime Implicants (PI) & Essential Prime Implicants (EPI)
Prime implicant is a group of ones (minterms) that cannot be combined with any other ones (minterms) or groups
EPI is PI, in which one or more minterms are unique
  i.e. it contain atleast one minterm which is not contained in any other PI

## Slide 78: Prime Implicant (Contd..)
 |  | 1 | 1
1 |  |  | 1
 |  | 1 | 1
 |  |  | 1
1 |  |  | 
1 |  | 1 | 
AB
C
00
01
11
10
0
1
Prime Implicant
00
01
11
10
00
01
11
10
BA
DC

## Slide 79: K-Map of 4 - variable

## Slide 80: Minimization of SOP Form

## Slide 81: Minimization of SOP Form
Determine the minimized expression in SOP form for the given truth table -
A | B | C | D | Y
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0

## Slide 82: Minimization of SOP Form (Contd..)

## Slide 83: Minimization of POS Form

## Slide 84: Minimization of POS Form
Minimize given truth table using Maxterm
A | B | C | D | Y
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0

## Slide 85: Minimization of POS Form (Contd..)

## Slide 86: Don’t Care Condition (X)
The K-Maps are simplified using either 1’s or 0’s, therefore we make the entries in the map for either 0 or 1
The cell which do not contain 1 are assumed to contain 0 & vice versa
This is not always true, since there are cases in which certain combinations of I/P variables do not matter

## Slide 87: Don’t Care Condition (X)
In such a situation the designer has a flexibility & it is left to him whether to assume 0 or 1 as O/P for each of these combinations
This condition is known as Don’t Care Condition and can be represented on K-Map as a X mark in the corresponding cell
The X mark in a cell may be assumed to be a 1 or 0 depending upon which one leads to a simpler expression

## Slide 88: Don’t Care Condition (X)
Without Considering don’t care conditions.
Y= AB’C
Assuming don’t care as 1.
Y=AC
POS form: Assuming don’t care as 0.
Y = A .C’

## Slide 89: Example

## Slide 90: Example
CD
AB
00 01 11 10
A’D + CD

## Slide 91: Example (Contd..)

## Slide 92: Example (Contd..)
Y = (A + B’) (A’ + C + D)

## Slide 93: BCD to Excess-3 Code conversion
B.C.D |  |  |  | Excess-3 |  |  | 
B3 | B2 | B1 | B0 | X3 | X2 | X1 | X0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | X | X | X | X
1 | 0 | 1 | 1 | X | X | X | X
1 | 1 | 0 | 0 | X | X | X | X
1 | 1 | 0 | 1 | X | X | X | X
1 | 1 | 1 | 0 | X | X | X | X
1 | 1 | 1 | 1 | X | X | X | X

## Slide 94
X3 =B3+B2 (B0+B1)
_ _ _ _
X2=B2B1B0 +B2B0 +B2B1
B1B0 B3B2 | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 0 | 1 | 1 | 1
11 | X | X | X | X
10 | 1 | 1 | X | X
B1B0 B3B2 | 00 | 01 | 11 | 10
00 | 0 | 1 | 1 | 1
01 | 1 | 0 | 0 | 0
11 | X | X | X | X
10 | 0 | 1 | X | X
B1B0 B3B2 | 00 | 01 | 11 | 10
00 | 1 | 0 | 1 | 0
01 | 1 | 0 | 1 | 0
11 | X | X | X | X
10 | 1 | 0 | X | X
B1B0 B3B2 | 00 | 01 | 11 | 10
00 | 1 | 0 | 0 | 1
01 | 1 | 0 | 0 | 1
11 | X | X | X | X
10 | 1 | 0 | X | X
_ _
X1= B0B1 +B0B1
_
X0= B0

## Slide 95
Multiplexer and Demultiplexer

## Slide 96: Multiplexer
Data Selector or Many to one circuit
Single IC

## Slide 97: Multiplexer
97
Types
  2:1 MUX
  4:1 MUX
  8:1 MUX
  16:1 MUX
(74157 / 74158 – Inverted I/P)
(74153 / 74352 – Inverted I/P)
(74151 / 74152 – Inverted I/P)
(74150 – Inverted I/P)

## Slide 98: Multiplexer
98
Advantages of Mux
  Reduces the number of wires
  Reduces circuit complexity & cost
  Minimize the IC package count

## Slide 99: 2:1 Multiplexer

## Slide 100: 2:1 Multiplexer Circuit

## Slide 101: 2:1 Multiplexer Circuit
Draw Gate level circuit diagram of 2:1 Multiplexer.

## Slide 102: 4:1 Multiplexer
Inputs |  |  | Output
E | S1 | S0 | Y
0 | X | X | 0
1 | 0 | 0 | I0
1 | 0 | 1 | I1
1 | 1 | 0 | I2
1 | 1 | 1 | I3
102

## Slide 103: 4:1 Multiplexer
103
Draw circuit diagram for 4:1 multiplexer using gates.

## Slide 104: Implement Circuit using MUX

## Slide 105: Implement Circuit using MUX

## Slide 106: IC 74153
(A)
(B)
Strobe (G’) Active Low | Select Inputs |  | Data Inputs |  |  |  | Y
 | B | A | D0 | D1 | D2 | D3 | 
H | X | X | X | X | X | X | L
L | L | L | L | X | X | X | L
L | L | L | H | X | X | X | H
L | L | H | X | L | X | X | L
L | L | H | X | H | X | X | H
L | H | L | X | X | L | X | L
L | H | L | X | X | H | X | H
L | H | H | X | X | X | L | L
L | H | H | X | X | X | H | H

## Slide 107: Multiplexer Tree
16-to-l multiplexers are the largest available lCs
To meet the larger input needs, multiplexers stack or trees are designed with the help of enable/strobe inputs.

## Slide 108: MUX Tree
Implement 4:1 Using 2:1

## Slide 109: MUX Tree (Contd..)
Implement 8:1 Multiplexer using 4:1 and 2:1 Multiplexer.
9

## Slide 110: Truth Table
S2 | S1 | S0 | Y
0 | 0 | 0 | I0
0 | 0 | 1 | I1
0 | 1 | 0 | I2
0 | 1 | 1 | I3
1 | 0 | 0 | I4
1 | 0 | 1 | I5
1 | 1 | 0 | I6
1 | 1 | 1 | I7
10

## Slide 111: Demultiplexer
11

## Slide 112: Demultiplexer
This circuit can also be used as binary-to-decimal decoder.
Binary inputs applied at the select input lines and the output will be obtained on the corresponding output line.
The data input line is to be connected to logic 1 level.

## Slide 113: Demultiplexer
This device is available as an MSI IC and can conveniently be used for the design of combinational circuits.
These devices are available as 2line-to-4-line, 3-line-to-8-line, and 4-line-to-I6-line decoders.
The outputs of most of these devices are active-low also there is an active-low enable/data input terminal available.

## Slide 114: Demultiplexer

## Slide 115: 1:2 Demultiplexer
12
Draw 1:2 Demultiplexer using gates.

## Slide 116: 1:4 Demultiplexer
S0
S1
D0 D1 D2
D3
I | 1: 4 DEMUX |  |  | 
E |  |  |  | 
E | S1 | S0 | D0 | D1 | D2 | D3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | I | 0 | 0 | 0
1 | 0 | 1 | 0 | I | 0 | 0
1 | 1 | 0 | 0 | 0 | I | 0
1 | 1 | 1 | 0 | 0 | 0 | I
13
4:1
DeMux

## Slide 117: Implement the Circuit
14
Draw 1:4 Demultiplexer using gates.

## Slide 118: Implementation of SOP using MUX
Implementation of 3 variable SOP expression using 8x1 MUX
A | B | C | X
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 119: Implementation of 3 variable SOP expression using 4x1 MUX (Reduction Method)
17
As only 2 select lines are available for 4:1 mux, there is a question of connection of one variable.
Lets connect B and C variables to S1 and S0 select lines of multiplexer.
Use reduction method to find where should third variable A should be connected.
F(A,B,C,D) = X = Ʃ m(0, 3, 4, 6)

## Slide 120: Implementation of 3 variable SOP expression using 4x1 MUX (Reduction Method)
I0 = Vcc, I1 = Gnd
I2 = A, I3 = A’

## Slide 121: Implementation of 4 variable SOP expression using 8x1 MUX (Reduction Method)
18
F(A,B,C,D) = X = Ʃ m(0, 2, 3, 8, 9, 10, 15)

## Slide 122
Decoder

## Slide 123: Decoder
A decoder is a logic circuit that accepts a set of inputs that represents a binary number and activates only the output that corresponds to the input number
In other words, a decoder circuit looks at its inputs, determines which binary number is present there, and activates the one output that corresponds to that number ; all other outputs remain inactive
In its general form, a decoder has N input lines to handle N bits and form one to 2 N output lines to indicate the presence of one or more N-bit combinations.
The basic binary function
An AND gate can be used as the basic decoding element because it produces a
HIGH output only when all inputs are HIGH

## Slide 124: General Decoder Diagram
# There are 2N possible input combinations, from A0 to AN1.
For each of these input combinations only one of the M outputs will be active HIGH (1), all the other outputs are LOW (0).

## Slide 125: General Decoder Diagram (Contd..)
If an active-LOW output (74138, one of the output will low and the rest will be high) is required for each decoded number, the entire decoder can be implemented with
    NAND gates
    Inverters
If an active-HIGH output (74139, one of the output will high and the rest will be low) is required for each decoded number, the entire decoder can be implemented with
    AND gates
    Inverters

## Slide 126: 2-to-4-Line Decoder (with Enable input)-Active LOW output

## Slide 127: 2-to-4-Line Decoder (with Enable input)- Active LOW output (Contd..)
The circuit operates with complemented outputs and a complement enable input. The decoder is enabled when E is equal to 0.
Only one output can be equal to 0 at any given time, all other outputs are equal to 1.
The output whose value is equal to 0 represents the minterm selected by inputs A and B
The circuit is disabled when E is equal to 1.

## Slide 128
74138 Decoder

## Slide 129: 4-line-to-16 line Decoder constructed with two 3-line-to-8 line decoders

## Slide 130: 4-line-to-16 line Decoder constructed with two 3-line-to-8 line decoders (Contd..)
When w=0, the top decoder is enabled and the other is disabled. The bottom decoder outputs are all 0’s , and the top eight outputs generate min-terms 0000 to 0111.
When w=1, the enable conditions are reversed. The bottom decoder outputs generate min-terms 1000 to 1111, while the outputs of the top decoder are all 0’s

## Slide 131: Half Adder & Full Adder
1

## Slide 132: Half Adder

## Slide 133: Half Adder Truth Table

## Slide 134: Circuit Diagram

## Slide 135: Half Adder USING 4:1 MUX :

## Slide 136: Full Adder

## Slide 137: Full Adder Truth Table

## Slide 138: Full Adder Circuit (Sum & Carry)

## Slide 139: Full Adder Circuit (Sum & Carry)

## Slide 140: Full Adder using Decoder
Let x, y and z represent these three bits. Sum and Carry outputs of a full adder have the following truth tables-
X | Y | Z | S | C
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 141: Full Adder using Decoder
Let x, y and z represent these three bits. Sum and Carry outputs of a full adder can be given as:
Assumption: Active high output decoder

## Slide 142: Logic Families
What is logic families?
  It is a group of compatible ICs with the same logic levels & supply voltages for performing various logic functions have been fabricated using a specific circuit configuration
Significance of logic families
  First and most important is simplicity in design
  It reduces the complexity in design
  Provide compatibility in digital circuit
  Easy to expand

## Slide 143: Characteristics of Digital IC
Speed of Operation
Power Dissipation
Figure of Merit
Fan-out
Fan-in
Current & Voltage Parameter
Noise Immunity
Operating Temperature Range
Power Supply Requirements

## Slide 144: Speed of Operation (Propagation Delay)
The speed of digital circuit is specified in terms of the propagation delay time
tpHL
tpLH
50%
50%
I/P
O/P
Fig: I/O Voltage waveforms to define Propagation Delay Times

## Slide 145: Speed of Operation (Propagation Delay) (Contd..)
The delay times are measured between the 50% voltage levels of I/O waveform
There are 2 delay times
  tpHL: O/P goes from the high state to low state
  tpLH: O/P making transition from low to high state
The propagation delay time(tp) of logic gate is taken as the average of these 2 delay times
2
tp =
tpHL + tpLH

## Slide 146: Power Dissipation
This is the amount of power dissipated in an IC
It is a measure of power consumed by the gate when fully driven by all its inputs
It is wastage of power across the circuit components.
It should be as low as possible.
It is measured in milliwatts
It is determined by current Icc that it draws from the Vcc supply
Power Dissipation (mW) = Vcc X Icc

## Slide 147: Power Dissipation (Contd..)
It is related to the power requirement of logic gate
Power dissipation is proportional to the heat generated by the system
Excessive heat dissipation may increase operating temperature & cause gate circuitry to drift out of its normal operating range

## Slide 148: Figure of Merit
The figure of merit of a digital IC is defined as the product of speed and power
The speed is specified in terms of a propagation delay time expressed in nanoseconds
Speed power product should be low
Figure of Merit = Propagation Delay X Power
pJ = ns X mW
ns – nano seconds
mW – milliwatts
pJ – pico joules

## Slide 149: Figure of Merit (Contd..)
For Example:
An IC has an average propagation delay of 20 ns & an average power dissipation of 5 mW
pJ = ns X mW
pJ = 20 X 5
pJ = 100

## Slide 150: Fan Out
This is the number of similar gates which can be driven by a gate
High fan out is advantageous because it reduces the need for additional drivers to drive more gates
The maximum fan out of an O/P, measures its load driving capability
The delay offered by a gate increases with increase in fan out
Fan In
It is total no. of inputs connected to any gate.
Two input gate – Fan in =2
Four input gate – Fan in =4

## Slide 151: Current & Voltage Parameter
High Level I/P Voltage (VIH):
  This is the minimum I/P voltage which is recognized by the gate as logic 1
Low Level I/P Voltage (VIL):
  This is the maximum I/P voltage which is recognized by the gate as logic 0
High Level O/P Voltage (VOH):
  This is the minimum voltage available at o/p corresponding to logic1
Low Level O/P Voltage (VOL):
  This is the maximum voltage available at o/p corresponding to logic 0

## Slide 152: Current & Voltage Parameter (Contd..)
High Level I/P Current (IIH):
  This is the minimum current which must be supplied by a driving source corresponding to 1 level voltage
Low Level I/P Current (IIL):
  This is the minimum current which must be supplied by a driving source corresponding to 0 level voltage
High Level O/P Current (IOH):
  This is the maximum current which the gate can sink in 1 level
Low Level O/P Current (IOL):
  This is the maximum current which the gate can sink in 0 level

## Slide 153: Current & Voltage Parameter (Contd..)
High Level Supply Current (Icc (1)):
  This is the supply current when the o/p of the gate is at logic 1 level
Low Level Supply Current (ICC (0)):
  This is the supply current when the o/p of the gate is at logic 0 level
IIL
IIH
IOL
IOH
Fig. Gate with current direction marked

## Slide 154: Noise Immunity
The circuit’s ability to tolerate noise signals is referred to as the noise immunity
It is the maximum noise voltage added to an i/p signal of a digital ckt that does not cause an undesirable change in ckt o/p
It is expressed in volts
Noise signals may cause the voltage at the i/p to a logic ckt to drop below VIH or rise above VIL & may produce undesired operation
A quantitative measure of noise immunity is called as a noise margin

## Slide 155: Noise Immunity (Contd..)
VoH (Min)
VoL (Max)
VIH (Min)
VoL (Max)
Logic 1
Logic 1
Logic 0
Logic 0
Intermediate I/P
Voltage range
Disallowed o/p voltage range
155

## Slide 156: Noise Immunity (Contd..)
VoH
VIH
VIL
VoL
1 State noise margin
0 State noise margin
1 = VoH - VIH
0 = VIL - VOL

## Slide 157: Operating Temperature Range
The temperature range in which an IC functions properly must be known
All gates or semiconductor devices are temperature sensitive in nature
The temperature in which the performance of IC is effective is called as operating temperature
Operating temperature of the IC vary from 00 C to 700C
The accepted temperature ranges are
  0 to +700C : for Consumer & Industrial operations
  -550C to +1250c : for Military purpose

## Slide 158: Power Supply Requirements
The supply voltage(s) and the amount of power required by an IC are important characteristics considered to choose the proper power supply.